SerLCD 16x2
14072, 14073
Engineer: Nathan Seidle
Test Dev: Pete Lewis 11/15/2016

1. Grab test fixture #579 (includes pogobed and Pi_grammer).
2. Power bed with 7V, 600mA
3. Power Pi_grammer via USB input.
4. Plug Pi_grammer into pogobed (3x2 AVR ISP header).
5. Place LCD screen on test jig. Close waffle top. Use clamp to hold down.
6. Tap “PRETEST & PWR”, and verify PRETEST PASS LED comes on.
7. Tap “PROGRAM” on Pi_grammer. Verify 3 pass LEDs (Fuse/Flash/Lock).
8. Tap “TEST” on pogobed. Verify PASS LED comes on.
9. Verify complete readout on screen.
10. Boards good. Power down.

*When you tap TEST, the following things are tested:
1. 3.3V output from product is correct.
2. Serial, I2C, and SPI ping tests.
3. Reset via DTR control pin.

*To see more granular test results/failures, listen to the Flying Jalapeno with an FTDI basic at 9600 BAUD.